## Slide 1: 1. Three transition scenarios/cases: Current measures, Canada net-zero, Global net-zero
We set the total CO2 emissions limits to describe these three sces
without splitting it to specific sectors (like agriculture), given it is hard to split the CO2 emissions from land-use and waste into specific sectors

## Slide 2: 2. Systemsetting
Time periods
Common commodities definition
Interpolation rules defaults
Other defaults and constant (like currency, for the test run we use EUR10 for the consistency with the open source EU-TIMES)
3. Base-year transformation
Shaping the tech transformation logs/history, including their change of efficiency/stock/available factor with time
The hydro/wind/PV were roughly estimated so far

## Slide 3: 3. Base year energy balance
Techs/processes for seven sector files of base-year were created
AGR\COM\IND\RSD\TRA: 2020 set as the base year, which is the latest year accessed from Natural Resources Canada website (the main data source)
ELC: Data mainly grabbed from EU-TIMES (the description for emissions for specific techs, and the transformations for heating)
SUP: Primary fuel data (coa/oil/gas resources constraints from CER2023, tech constraints referring EU-TIMES, RES were roughly estimated so far)

## Slide 4: 3. Base year energy balance
Limited by the NRC data source
Atlantic as a whole province (we didn’t split it into NB, NL..)
BC and TE as a whole province

## Slide 5: 4. New techs: The hydrogen, CCUS, power storage, and other new power techs were introduced from EU-TIMES, after minor-revision to adapt to the model commodity and process sets

## Slide 6
4. The ELC/GAS/OIL/COAL imports and exports to USA are introduced as a tech, with data sourced from CER2023, but some constraints need to be detailed more (like the bound for transmission).

## Slide 7
5. Interprovincial trading
Limited by the CER 2023 data (which only detailed the inflow/outflow for specific province, like how much in total did BC import, but without the importing source)
We split the inflow/outflow (specific starting point and destination), by using the other trading information from google-search
New Brunswick only imports from Quebec, so we can derive the flow from Quebec to NB
The Quebec export to other provinces (except NB) could be derived
Step by step, the trading link and detailed quantity could be derived

## Slide 8
Some other detailed assumptions attached in this slides to supplement the annotations in Excels, for base-year files

## Slide 9
The Annual Production Bound for the mining coal/gas/crude oil (i.e. mining capacity)
*29.3 GJ/tonne hard coal, while 15 GJ/tonne lignite coal, referring to https://www150.statcan.gc.ca/n1/pub/57-601-x/2011003/appendix-appendice1-eng.htm
Coal production logs (unit:tonne) access in:
https://www150.statcan.gc.ca/t1/tbl1/en/tv.action?pid=2510004601&pickMembers%5B0%5D=1.3&cubeTimeFrame.startMonth=01&cubeTimeFrame.startYear=2008&cubeTimeFrame.endMonth=12&cubeTimeFrame.endYear=2023&referencePeriods=20080101%2C20231201
*assuming the mining capacity doesn't change with time
*assuming the production bound will shrink 90.15% in the second step of mining coal, compared with the first step, as indicated by EU-27; and we adopt similar assumption for oil, gas, by quantifying the shrink rate of EU-27

## Slide 10
The Annual Production Bound for the mining coal/gas/crude oil (i.e. mining capacity)
*referring the 2020 practical gas production of canada energy future report 2023; and *3.73*10^-5 PJ/ m3 gas, referring to https://apps.cer-rec.gc.ca/Conversion/conversion-tables.aspx?GoCTemplateCulture=en-CA
*referring the 2020 practical crude oil production of canada energy future report 2023; and 0.039356 PJ/m3 as the average of the values in https://apps.cer-rec.gc.ca/Conversion/conversion-tables.aspx?GoCTemplateCulture=en-CA

## Slide 11
The Reserves Cumulative Value for the mining coal/gas/crude oil
Canada's coal proved reserves amounted to roughly 6.6 billion metric tons in 2020, which is as indicated in https://www.statista.com/statistics/265436/proved-coal-reserves-in-canada/#:~:text=Canada%27s%20coal%20proved%20reserves%20amounted%20to,roughly%206.6%20billion%20metric%20tons%20in%202020; While 39.55 million metric tons are produced in 2020 (https://www.ceicdata.com/en/indicator/canada/coal-production#:~:text=Canada%20Coal%20Production%20was%20reported%20at%2039.550%20Tonne,from%20Dec%201981%20to%202020%2C%20with%2040%20observations). So the Cumulative value is nearly about 165 times of 2020 production
Canada had 2.4 trillion cubic meters of natural gas reserves in 2020, https://www.bing.com/ck/a?!&&p=74307da1a79fceddJmltdHM9MTcwNDkzMTIwMCZpZ3VpZD0xYmYxMWEyOS00Njg2LTZjM2MtMzE4MC0wOWYyNDcwYzZkZTQmaW5zaWQ9NTIwNA&ptn=3&ver=2&hsh=3&fclid=1bf11a29-4686-6c3c-3180-09f2470c6de4&psq=Reserves+Cumulative+Value+for+gas+in+canada%2c2020&u=a1aHR0cHM6Ly93d3cuc3RhdGlzdGEuY29tL3N0YXRpc3RpY3MvMjY1MzIxL3Byb3Zlbi1uYXR1cmFsLWdhcy1yZXNlcnZlcy1pbi1jYW5hZGEtaW4tdHJpbGxpb24tY3ViaWMtbWV0ZXJzLw&ntb=1; while the production is about 15.5 billion cubic feet per day, https://www.bing.com/ck/a?!&&p=2e12b6968e360a5fJmltdHM9MTcwNDkzMTIwMCZpZ3VpZD0xYmYxMWEyOS00Njg2LTZjM2MtMzE4MC0wOWYyNDcwYzZkZTQmaW5zaWQ9NTQ2Mg&ptn=3&ver=2&hsh=3&fclid=1bf11a29-4686-6c3c-3180-09f2470c6de4&psq=production+for+canada+gas%2c+2020&u=a1aHR0cHM6Ly93d3cuY2VyLXJlYy5nYy5jYS9lbi9kYXRhLWFuYWx5c2lzL2VuZXJneS1tYXJrZXRzL3Byb3ZpbmNpYWwtdGVycml0b3JpYWwtZW5lcmd5LXByb2ZpbGVzL3Byb3ZpbmNpYWwtdGVycml0b3JpYWwtZW5lcmd5LXByb2ZpbGVzLWNhbmFkYS5odG1sIzp-OnRleHQ9TmF0dXJhbCUyMEdhcyUyRk5hdHVyYWwlMjBHYXMlMjBMaXF1aWRzJTIwJTI4TkdMcyUyOSUyMDElMjBJbiUyMDIwMjAlMkMsT250YXJpbyUyQyUyMGFuZCUyMHRoZSUyME5vcnRod2VzdCUyMFRlcnJpdG9yaWVzJTIwJTI4TldUJTI5LiUyME1vcmUlMjBpdGVtcw&ntb=1. which is about 150 times.
In total, Canada's established remaining oil reserves amounted to 166.7 billion barrels as of 2020, https://www.statista.com/statistics/973765/canadian-oil-reserves-by-type/#:~:text=In%20total%2C%20Canada%27s%20established%20remaining%20oil%20reserves,amounted%20to%20166.7%20billion%20barrels%20as%20of%202020; Canada produced 4.66 million barrels per day (MMb/d) of crude oil in 2020, https://www.bing.com/ck/a?!&&p=a706b9492ee78d9fJmltdHM9MTcwNDkzMTIwMCZpZ3VpZD0xYmYxMWEyOS00Njg2LTZjM2MtMzE4MC0wOWYyNDcwYzZkZTQmaW5zaWQ9NTQ4MA&ptn=3&ver=2&hsh=3&fclid=1bf11a29-4686-6c3c-3180-09f2470c6de4&psq=production+for+canada+oil%2c+2020&u=a1aHR0cHM6Ly93d3cuY2VyLXJlYy5nYy5jYS9lbi9kYXRhLWFuYWx5c2lzL2VuZXJneS1tYXJrZXRzL3Byb3ZpbmNpYWwtdGVycml0b3JpYWwtZW5lcmd5LXByb2ZpbGVzL3Byb3ZpbmNpYWwtdGVycml0b3JpYWwtZW5lcmd5LXByb2ZpbGVzLWNhbmFkYS5odG1sIzp-OnRleHQ9Q3J1ZGUlMjBPaWwlMjAxJTIwQ2FuYWRhJTIwcHJvZHVjZWQlMjA0LjY2JTIwbWlsbGlvbiUyMGJhcnJlbHMsZ29lcyUyMHByaW1hcmlseSUyMHRvJTIwZXhwb3J0JTIwbWFya2V0cy4lMjAuLi4lMjBNb3JlJTIwaXRlbXM&ntb=1. which means that the cumulative value is about 100 times

## Slide 12: The annual production activity for the refining oil (assumption)
*For the annual production bound (ACT_BND) of the refinery for crude oil, we compared the base-year total production and the capacities of refineries in a specific province (like Quebec), and we choose the bigger one as the boundary
* for example, the data source indicated that quebec has no commercial crude oil production, but it shows that Two large refineries currently operate in Quebec with a combined capacity of 372 thousand barrels per day (Mb/d), which is 830.63 PJ

## Slide 14: For systemsetting: Blue and yellow background marks the tracking revision Brown background denotes the * useless information (just for reference)

## Slide 15
Cost was referred to as the average of EU-27
The cost/output shares for the mining coal/gas/crude oil, and the generation costs for geo/hydro/wind/solar

## Slide 16
Cost was referred to as the average of EU-27
Refining oil: the share of these output commodity- oil types (like heavy oil, LPG, etc.) are the average of EU-countries
Refining oil: the other input were also referred to EU-TIMES, including
INDELC
REFHTH
SUPBIO
SUPCOA
SUPRPG
SUPRPP
The cost/output shares. for the refining oil (assumption)

## Slide 17: Assume for agr sector: the data source split it as motive energy use and non-motive energy use, we consider the motive energy use is only from diesel and gasoline. Because the proportion of sum of diesel and gasoline eq to 0.55 (FOR AT, FOR EXAMPLE), which is same as the results of motive sum use/total use.
steam energy (data source for Canada) is a specific form of heat energy (from EU-TIMES) associated with the vaporization of water. So we could assume the commodity-in is HET, same with EU-TIMES
AGR
BC denotes BC&TE

## Slide 18: Main assume is about the Efficiency for light is 0.8 & Available factor is 0.1
COM
Commodity input
Combustion efficients refers to EU-TIMES, and the lacking data is grabbed from google search

## Slide 19
COM
WHY FROM PJ TO PJA, need to multiply 1.05

## Slide 20
note: the technologies for indstry-subsectors are reduced to 1 process & limited number of techs
IND
The unclear energy consumption (shown with X) was assumed to be zero
ASSUMING EFF AS 1.0, AND available factor as 1.0, and the stock unit is PJa
We lack the production data for iron/steel (unit:Mt), so we have detailed it in the input data

## Slide 21
RSD
1. The calculation for AFA may have some faults
2. The RES_FUEL: ~FI_T: Share~UP totally referred the EU_TMES----- need to be revised, for example, the input shares for RSD_COAPRO00 need to be revised because the PROP has not been considered
HAVE NOT CONSIDERED NEW TECHNOLOGIES LIKE new gas techs, in this folder, same for other sectors::which is different with EU-TIMES
DeACTFI_T: Stock ??
3. For all sectors, the EMI we have not considered the static combustion coefficient, because we don’t know what it is, to avoid the bug so we deleted it… but EU-TIMES have considered it

## Slide 22
(seems not necessary)1. act_flow=consumption split(ktoe)/EFE
2. NCAP_AFA=correction factor*
F292(!!average factor)*F$286(correction factor, couold be set as 1)*1.15
what we have:
4 types of household,
5 types of end-use and their PJ (after table 34)
4*5 end-use type stocks (Table 21-31)
ASSUMING:
////4*heating*10 end-use and energy source techs for stocks (Table 22-25), and the efficiencies (Table 26)[the split consumption of like, oil for SingleAttached and SingleDetached is same, both equal to the total oil consumption/total energy consumption]
////4*cooling*2 end-use&energy source stock and energy efficiency (Table 27)[assuming all 4 types of household use the same proportion of room and central][assuming the capacity for room is 2kw, while that for central is 5mw, refeereing to EUTIMES][when calculating AFA, BASED ON THE ENERGY CONSUMPTION PJ/STOCK MW, we need to devide the 31.54 as PRA_ACTVITY;;AND THE PJ is splited as the observed stock proportion]
////4*water heating*6 end-use&energy source stocks /// but no EFF, (Table 29-30)[so assume it to 0.65 firstly, which is the minimum threshold as specified in EUTIMES][and assuming the cap is 2kw, referred to the ..]
////4*appliance*7 end-use&energy source stocks ///but no EFF (Table 31)[so assume it to 1]
/// assume: only consider that all appliance is powered by electricity, because the gas-powered could be ignored, 0.1PJ-GAS vs. 14.1PJ-electricity
(their capacity adopts the median of google range) [efficiency was set as ..][assume the AFA=total PJ/total stock because we only have PJ data]
///[assuming each household install 5kw of lighting]
//how to transfer the stock (unit:1) to capacity stock (unit:GW)-- just assume every type is 1 kw or referring to EUTIMES
?? how to assume the AFA
(by dividing sum pj for this type/gw,)
conclusion:
we still don't know what is 31.54 for ??
THE RES_FUEL AND EMI totally referred to the EU-TIMES?
how to define dual technology !!
RSD (additional)
Lifetime for appliance like washing machine is 10-years, defined in By_Trans: Data rules

## Slide 23
ELC
Totally referring to EU-TIMES, even not change the cost, because the value for 1 Europe similar to 1$
We define the electricity as ELC no matter with medium Voltage or High Voltage
EFF for heating from electricity is set as the average of EU-27 from EU-TIMES, 83%;;; no CAP_BOUNT, which is different with EU-TIMES

## Slide 24
TRA
Occupancy--ACTFLOW (carried passenger number/ specific vehicle number-like bus), and the number is referred to the EU-TIMES:
000Veh_STOCK, the block in the red background, is from the data source? But the data for BC has lost
This sector has detailed the energy split for the four provinces of Atlantic region, while only the sum was described in other sectors, therefore, we consider the Atlantic as one whole body; and the data source describe BC&TE as a whole body, which we denote it as BC in our model
Aviation: The transfer coefficient from PJ to mio tkm (freight air) is the average of EU-27 (169.2 mio tkm/PJ) ; while that for passenger air is 625.1 mio pkm/PJ.. But the two numbers were calculated without considering the types for the consuming energy …. Assuming the turbo fuel is produced from heavy fuel oil
Nav: 3176.1 million tkm/PJ, also derived from EU-TIMES
rail: 123 million tkm/PJ for diesel freight rail, while 39 million pkm/pj for diesel passenger rail, because natural resources Canada declare that the rails only consume diesel, these two data also averaged by EU-27 (actually they split it to 37 regions)
Some Unit transfer efficient, 31.5 or 1 (NEED TO RE-CHECK, to ensure the same with EU-TIMES)?
AF for road vehicle is referred to EU-TIMES (km/veh), and the ability to carry passenger (passenger number/ vehicle) is referred to EU-TIMES
We could only access the total stock for passenger light truck, including gasoline-fueled and diesel-fueled types, we assume their proportion as 80% and 20%, because Gasoline engines are generally quieter and lighter than diesel engines, making them suitable for the driving characteristics desired in many passenger-oriented vehicles.
Gasoline engines have been the primary choice for small cars due to factors such as smoother operation, lower noise levels, and ease of starting. Gasoline-powered engines are also generally lighter and less expensive to produce, which contributes to their popularity in smaller vehicles. So we assume the stock for gasoline-powered car is 100%
Buses commonly use diesel fuel, especially larger buses such as transit buses, intercity buses, and school buses. Diesel engines offer several advantages for buses, including better fuel efficiency and more torque, which is important for moving heavy loads and negotiating frequent stops.
Not sure about ~FI_T: Demand in 000Veh
And timeslices need to be re-checked?? (GAS is season, while elc is daynite, but why steam is season, should we revise it from default to season ?)
Lifetime for Trai, Tavi, and Tnav, is 20-years, defined in By_Trans: Data rules
Find if the parameters for all commodities are complete?

## Slide 25: NEW TECHS : We use Europe yuan as currency firstly
All tech-tran files need major revisions, we have only included one trans for test; and we have only included significant new technologies for test, including CCUS, hydrogen, power storage, and ..
The green background marks the tracking-revision, without marking the change from ELCHIG to ELC in CCUS techs
The techs for import and export to USA (like the bound for transmission) should be detailed more.

## Slide 26
sysetting: import setting, we don’t know what it is
!Interpol_Extrapol_Defaults